## Slide 1: Divide & Conquer

## Slide 2: Strategy
Narrow the search with successive approximation. Guess a number from 1 to 100, in seven guesses.
Get the range. If the number is 135 and you think the range is 1 to 100, you'll have to widen the range.
Determine which side of the bug you are on. If there's goo, the pipe is upstream. If there's no goo, the pipe is downstream.
Use easy-to-spot test patterns. Start with clean, clear water so the goo is obvious when it enters the stream.
Start with the bad. There are too many good parts to verify. Start where it's broken and work your way back up to the cause.
Fix the bugs you know about. Bugs defend and hide one another. Take 'em out as soon as you find 'em.
Fix the noise first. Watch for stuff that you know will make the rest of the system go crazy. But don't get carried away on marginal problems or aesthetic changes

## Slide 3: Change One Thing at a Time

## Slide 4: Strategy
Isolate the key factor. Don't change the watering schedule if you're looking for the effect of the sunlight.
Grab the brass bar with both hands. If you try to fix the nuke without knowing what's wrong first, you may have an underwater Chernobyl on your hands.
Change one test at a time. I knew my VGA capture phase was broken because nothing else was changing.
Compare it with a good one. If the bad ones all have something that the good ones don't, you're onto the problem.
Determine what you changed since the last time it worked. My friend had changed the cartridge on the turntable, so that was a good place to start

## Slide 5: Keep an Audit Trail

## Slide 6: Strategy
Understand that any detail could be the important one. It had to be a plaid shirt to crash the video chip.
Correlate events. "It made a noise for four seconds starting at 21:04:53" is better than "It made a noise."
Understand that audit trails for design are also good for testing. Software configuration control tools can tell you which revision introduced the bug.
Write it down! No matter how horrible the moment, make a memorandum of it.